WAC Away Cell Launch System

Setup:

( raise data cable reel transportation handle for wheeling

( set Controller box on LCO table & data reel within 6’

( disconnect & retain data reel cable clip/bungee

( reel out data cable up to 1000’ to away cell; pull on cable, not connector

( set Launch box 25’ from away cell

( Connect:

• Controller box < -- > 6’ data cable < -- > data reel

• away cell data cable < -- > Launch box

• Launch box < -- > Pads 1 - 3 ignition leads

( “Power” up Launch box (can stay powered all day)

Launch:

( verify Controller box is off

( connect ignition leads to igniter

( “Test” continuity with red button on Launch box

( “Power” up Controller box

( “Enable” the system (must be on for any other operations)

( “Arm” any combination of Pads 1 - 3

( Optionally trigger remote “Alarm” to alert pad area

( “Fire”

( “Power” off Controller box after each launch!

Notes:

( red LED is local, green LED is data loop validation

( green LED will delay 1/2 second after each switch change

( each Pad has a 15 amp manual “Reset” circuit breaker

( the Launch box has a 50 amp self-resetting circuit breaker; remove short circuit & wait 30 seconds

( the Launch box can have external batteries attached

Breakdown:

( Power off Launch box - LED will delay 10-20 seconds

( disconnect all cables, stow 6’ data cable & launch leads

( clean inside of Launch box before closing

( reel up data cable; work back and forth for even lay-up; do not drag connector cross-country!

( secure data cable with clip/bungee

( pull tab on data cable reel winder handle to collapse

( push tabs on data cable reel transportation handle to collapse

# Maintenance:

( charge Launch box batteries before each launch & every launch night

( charge Controller box every 2-3 months, before each launch & every launch night